# 16. Blisks

### Introduction

In New strategies, the Blisks option provides 3 specialist strategies for machining Impellers.

### Impeller Example

Select File - Delete All

Select Tools - Reset Forms

Open the ‘read only’ Project:-

D:\users\training\PowerMILL_Data\FiveAxis\Blisks\BliskSimple_Start

Select File - Save Project as:-

D:\users\training\PowerMILL_Data\FiveAxis\Blisks\BliskSimple_Example

Activate Workplane 1.

Create a Cylindrical Block to the Model dimensions.

Reset the Rapid Move Heights.

Set both Start and End Points to First/Last Point Safe Z.

In the Leads and Links form set all Links to Skim.

To be able to apply the Blisks machining options the component surfaces must first be acquired to a series of specifically named levels. In this example the surfaces in the imported model are already acquired to appropriate levels.

HUB              RH BLADE       LH BLADE       SHROUD

Activate the existing Ball Nosed tool Named BN25.

Open the Default Thickness form  and then select the Surface Defaults tab.

Select the Shroud Surface and acquire          it to the first row in the above form.

Set the first row to Machining Mode Ignore and Apply the settings, before closing the form by clicking Accept.

In the Tooplath Strategies form, select Blisks and from the three available options, select Blisk AreaClear Model.

Enter data exactly as shown below with the Fillets and Splitter Blade options left blank.

Select Queue in the form to commence background processing.

Activate the existing Ball Nosed tool Named BN15.

In the Tooplath Strategies form, select Blisks and from the three available options, select Blade Finishing.

Enter data exactly as shown below with the Fillets and Splitter Blade options left blank.

Select Queue in the form to commence background processing.

In the Tooplath Strategies form, select Blisks and from the three available options, select Hub Finishing.

Enter data exactly as shown below with the Fillets and Splitter Blade options left blank.

Select Queue in the form to commence background processing.

Once all of the 3 toolpaths have been created, perform a full ViewMILL simulation on the project.

Before running ViewMILL it is necessary to define the Block as a Triangle model of the Pre-turned, Shroud for an accurate representation of the material prior to milling.

In the Block form select Defined By - Triangles and select the Load block from file icon (arrowed).

Browse and select the Triangle file:-

D:\users\training\PowerMILL_Data\FiveAxis\Blisks\TurnedShroud.dmt

With the complex Block active, switch on a ViewMILL simulation.

Right mouse click on Toolpath BN25-Rgh-a1 and select Simulate from Start before clicking on the Play icon in the toolpath Simulation toolbar.

Continue the ViewMILL simulation on Toolpath BN15-fin-a1.

Continue the ViewMILL simulation on Toolpath BN15-finHUB-a1.

The final image (below) shows the result of a ViewMILL simulation using Copies of the toolpaths transformed by 20 Degree increments around Z.